## Slide 1: CBE255 Discussion 10 4/8/21
Turner Luke
* If you are not registered for this discussion, let me know so I can send you the presentation

## Slide 2: Reminders
Homework 8 due Tomorrow
  Please submit a single PDF
I can’t stay late after OH tonight
  I don’t anticipate it will be busy, but coming early will guarantee I get to your question
  Or use the extra time after discussion

## Slide 3: Agenda
Questions?
Integration
Combining Integration and Interpolation
HW8Q3 Help

## Slide 4: Recall Elementary Calculus
Recall Riemann Sum

## Slide 5: Pre-Coded Integral Solvers
MATLAB
  1 Dimensional
  q = integral(fun,xmin,xmax)
  2 Dimensional
  q = integral2(fun,xmin,xmax,ymin,ymax)
Python
  1 Dimensional
  scipy.integrate.quad(func, a, b)
  2 Dimensional
  scipy.integrate.dblquad(func, a, b)

## Slide 6: Code a Function Calculating the Error Function
Validate your results with a native error function

## Slide 7
import numpy as np from scipy.integrate import quad from scipy.special import erf def error_function(x): return 2 / np.sqrt(np.pi) * quad(lambda t: np.exp(-t**2), 0, x)[0] print(error_function(5)) print(erf(5))
disp(error_function(5))
disp(erf(5))
function F = error_function(x)
f = @(t) exp(-t.^2);
F = 2 / sqrt(pi) * integral(f,0,x);
end

## Slide 8: Interpolation with Data
1: Create a function with the data f(x)
  Select interpolation method that best matches the physical concepts behind the data
  f = @(x) interp1(xdata, ydata, x, ‘method’)
  f = scipy.interpolate.interp1d(xdata, ydata, kind=“method”)
2: Pass the interpolation function in an integral method

## Slide 9: CBE 426 Example
The height of a packed column is equal to the height of a transfer unit by the number of transfer units
Depending on the basis of your packed column: (Overall, Gas)

## Slide 10
import numpy as np from scipy.interpolate import interp1d from scipy.integrate import quad y = np.array([0, 0.005, 0.02, 0.05, 0.10, 0.15, 0.20]) ys = np.array([0, 0, 0.005, 0.016, 0.038, 0.066, 0.097]) ys_of_y = interp1d(y, ys) def f(y): return 1 / (1 - y) / (y - ys_of_y(y)) N = quad(f, 0.002, 0.18)[0] H = 2.5 Z = H * N print("The required height of packing is {:.2f} m.".format(Z))

## Slide 11
y_data = [0, 0.005, 0.02, 0.05, 0.10, 0.15, 0.20];
ys_data = [0, 0, 0.005, 0.016, 0.038, 0.066, 0.097];
ys_of_y = @(y) interp1(y_data, ys_data, y, 'spline');
f = @(y) 1 ./ (1 - y) ./ (y - ys_of_y(y));
N = integral(f, 0.002, 0.18);
H = 2.5;
Z = H * N;
fprintf("The required height of packing is %.2f m.", Z)

## Slide 12: Rayleigh Equation (CBE426)
Batch Still
x
Condenser
Receiver
XD
Q
Q
Moles of A in still
Material balance around still
Change of A = fraction A in flow out * flow out
Equate (Subscripts dropped)
Separate, Integrate.

## Slide 13
Mass/Material Balances
Recovery
* 100%

## Slide 14: Project 3 “Above and Beyond”: LaTeX
LaTeX is a software system for document preparation.
Like much of the things we do in this class, LaTeX is more powerful than typical methods, but less user friendly
https://www.overleaf.com/learn/latex/Learn_LaTeX_in_30_minutes